## Slide 1
Adam Gryko & Will Smith
11/05/2020
Open EVR Progress

## Slide 2
Image © STFC John Dawson
Aims
Take the firmware released by Jukka and implement it
  https://github.com/jpietari/mrf-openevr
  http://www.mrf.fi/pdf/workshop2017/Jukka.pdf
Understand hardware requirements
By implementing it understand more about how EVR works
Add to the MRF open EVR firmware
  Add timestamping functionality
  Add ability to decode data bus
  Add FIFO that timestamps received events from the bus
Build development infrastructure (Petalinux)

## Slide 3
Image © STFC John Dawson
Open EVR
What it is
  Firmware to decode MRF timing protocol
  Recover the event clock
  Receive event codes
  Delay Compensation
What it is not
  Hardware replacement for existing MRF products
  bus/ register interface for mrfioc2
  pulse generators, sequencer etc

## Slide 4
Image © STFC John Dawson
Possible Use Cases
Data acquisition with synchronous sample clock with 10’s picosecond timing jitter.
Synchronous triggering of firmware from events for physically distributed systems.
Timestamping of acquired data or events within firmware design
Not a replacement for standalone EVR’s and output modules for interface with systems that take TTL triggers

## Slide 5
Image © STFC John Dawson
Hardware Requirements
Xilinx Kintex-7 based FPGA with GTX transceivers.
  Applicable for the released firmware only. This is not a general requirement of a DC EVR. Other EVR’s with delay compensation have been implemented with various FPGAs and Transceivers (PSI). See later slides
SFP Transceiver
Reference clock for the GTX transceiver

## Slide 6
Image © STFC John Dawson
Development System
Picozed with 7Z030
Carrier card with SFP transceiver (and FMC)
Network connected JTAG for programming
Power Supply
Raspberry Pi to monitor the serial output of the device.

## Slide 7
Image © STFC John Dawson
Implementation
We implemented this
And used this to investigate integration with the PS

## Slide 8
Sync
Image © STFC John Dawson
Timestamping
32-bit Seconds Register
32-bit Timestamp Counter
32-bit Seconds | 32-bit Timestamp | Event
32-bit Seconds | 32-bit Timestamp | Event
¦ | ¦ | ¦
32-bit Seconds | 32-bit Timestamp | Event
32-bit Seconds Shift Reg
reset
Event Clock
Reset Event (0x7D)
Load 0 (0x70)
Load 1 (0x71)
Notes: https://github.com/whs92/mrf-openevr/blob/master/ip/openevr_event_timestamp/openevr_event_timestamp.srcs/sources_1/new/event_timestamp.vhd

## Slide 9
Image © STFC John Dawson
Data-bus
Implemented by existing open EVR Firmware
  https://github.com/jpietari/mrf-openevr/blob/master/vhdl/databuf_rx_dc.vhd
We tested it using the ILA

## Slide 10
Image © STFC John Dawson
Testing
EVG
83 MHz
1PPS
VME EVR
IFC1210, mrfioc2
Open EVR
Petalinux, monitor.c
Set up a test system
  Clock
  1PPS
VME EVR used mrfioc2 to expose timestamps of received events codes.
OpenEVR ran a script on the PS in Petalinux OS that monitors events and their timestamps (interrupt driven.)
They were the same!

## Slide 11
Image © STFC John Dawson
PSI Implementations
Koprek Waldemar (PSI) waldemar.koprek@psi.ch

## Slide 12
Image © STFC John Dawson
PSI Implementations

## Slide 13
Image © STFC John Dawson
What’s Next
STFC unlikely to continue development in the near future. Adam Gryko has left and I am leaving in September to got to BESSY. Contact graham.cox@stfc.ac.uk
Source code available on git-hub https://github.com/whs92/mrf-openevr
Can be integrated into a firmware design that has access to correct oscillator and GTX transceivers.
Interface to PS (Petalinux) and some register control and interrupt handling.
Is compatibility with something like mrfioc2 even useful? Applications that require embedded EVR’s need timestamp, clock, and maybe to respond to particular triggers. I think aim should be to keep it light weight!